## Slide 1
🦺
M.Tech CSE · RGIPT · 2026
Kunal Kumar Gupta
Roll No: 23MC3035
Real-Time AI-Powered
PPE Compliance
Monitoring System
Intelligent Industrial Safety for Tata Steel Manufacturing Environments
"Zero tolerance for non-compliance"
7
System Stages
0.978
mAP@0.5
4
PPE Classes
<1s
Alert Latency
1 / 12

## Slide 2
Problem Statement
2 / 12
2.3M
occupational deaths / year
Source: ILO Global Estimates
👷 Manual Monitoring
Security guards checking PPE at entry points — slow, inconsistent, and prone to human error. Coverage is limited to single checkpoints.
⏱️ Delayed Response
Violations detected minutes or hours later via CCTV review — not in real-time. Workers at risk during the gap between violation and intervention.
📊 No Analytics
No historical data, no per-worker tracking, no pattern analysis. Safety managers cannot identify repeat offenders or high-risk zones.
Current solutions are expensive, non-real-time, and limited to a single camera angle — unsuitable for large manufacturing floors

## Slide 3
Proposed Solution
3 / 12
From violation to alert in under 1 second
🎯
Dual-Model AI Pipeline
YOLOv8n — person detection (COCO pretrained)
YOLOv8s — custom PPE detection
Helmet · Safety Vest · Goggles
IoU-based spatial association
🔔
Instant Alert System
Per-worker streak tracking
Alert fires in < 8 non-compliant frames
Auto-screenshot with every alert
WhatsApp via Meta Cloud API
📊
Live Dashboard
FastAPI + WebSocket backend
Real-time violation feed < 1s
Stats cards + screenshot viewer
Dark-theme SPA — no build step
🏭
Production Ready
Multi-camera via cameras.yaml
SQLite WAL for concurrent writes
Docker CPU + NVIDIA GPU builds
FP16 / ONNX / TensorRT export

## Slide 4
System Architecture — 7-Stage Pipeline
4 / 12
1
📹
Video
Source
▶
2
👤
Person
Detector
▶
3
🦺
PPE
Detector
▶
4
✅
Compliance
Checker
▶
5
🚨
Alert
Engine
▶
6
💾
DB + WA
Logger
▶
7
📊
FastAPI
Dashboard
Webcam / MP4
/ RTSP
YOLOv8n
(COCO)
YOLOv8s
(custom)
IoU-based
association
Streak
tracking
SQLite WAL
+ Meta API
FastAPI
+ WS
Two parallel processes share one SQLite DB via WAL mode
Compliance decision made per-frame, per-worker, in-process
WhatsApp alerts fire asynchronously — pipeline never blocks

## Slide 5
Dataset & Model Training
5 / 12
📦 Dataset Composition
5
Merged Roboflow datasets
30,473
Total images (640×640)
4
Classes: Helmet · Safety Vest · Goggles · Gloves
36
Background images (test)
366
Test-split images
Sources: Roboflow Universe, custom CCTV footage (Tata Steel)
⚙️ Training Configuration
Model:
YOLOv8s (custom fine-tuned)
Epochs:
100
Batch:
16
Optimizer:
AdamW + cosine LR decay
Augmentation:
mosaic, flip, scale, hsv
Train HW:
NVIDIA RTX A5000 (Windows)
Deploy HW:
Apple M1 Pro MPS (macOS)
Inference:
336 ms/image on CPU

## Slide 6
Model Performance — Test Split (366 Images)
6 / 12
0.978
mAP@0.5
0.980
Precision
0.970
Recall
0.781
mAP@0.5:0.95
Per-Class Results
Goggles
0.988
PASS ✓
Safety Vest
0.994
PASS ✓
Helmet
0.952
✓ PASS
Evaluation Config
Test images:
366
Backgrounds:
36
Conf threshold:
0.25
IoU threshold:
0.50
Inference time:
336 ms/img
Hardware:
M1 Pro CPU
▲ target = 0.850

## Slide 7
Key Feature — Intelligent Alert Engine
7 / 12
👤
Person detected
▼
🔍
PPE checked (IoU)
▼
❌
Non-compliant frame
▼
🔢
Streak count +1
▼
🚨
Alert fires @ N frames
▼
📸
Screenshot + WhatsApp
⏱️
< 0.67 s to alert
Alert fires after 20 consecutive non-compliant frames at 30 FPS — under two-thirds of a second from first violation.
🔒
60-second cooldown
Per-worker cooldown prevents alert spam. Same worker re-triggers only after 60 seconds of continued violation.
📍
Spatial hash IDs
Workers are identified by their bounding-box centroid grid cell — no ByteTracker dependency. Works reliably at fixed camera angles.
🎨
Visual HUD + flash
Live window shows red flash border on alert, per-worker boxes annotated with compliance status and missing PPE labels.

## Slide 8
Live Dashboard — FastAPI + WebSocket
8 / 12
🦺 PPE Compliance Monitor
🗑 Clear All
44
Total
12
Critical
32
Warnings
8
Today
Time Worker ID Missing PPE Severity Screenshot
14:32:11
W-03
helmet, safety_vest
CRITICAL
🖼
14:31:55
W-01
safety_vest
WARNING
🖼
14:30:48
W-05
goggles
WARNING
🖼
● LIVE – WebSocket connected – Last update: 0.3s ago
Dashboard Features
🔴
Real-time WebSocket updates
New alerts appear in < 1 second without page refresh
📊
Stat cards
Total, Critical, Warnings, Today's count auto-refreshed
🦺
PPE breakdown
No-helmet / No-vest / No-goggles individual counters
🖼️
Screenshot viewer
Click any row to open full screenshot in a modal
🔍
Severity filter
Filter table by CRITICAL / WARNING severity
📋
Sessions table
Pipeline run history with start times and DB row counts
🌑
Dark SPA
Tailwind CSS CDN — no build step, works in any browser

## Slide 9
Multi-Camera & Docker Deployment — Stage 7
9 / 12
📹 Multi-Camera (cameras.yaml)
📷 Gate-1 Camera
rtsp://192.168.1.100/stream
requires: helmet, safety_vest
📷 Welding Bay
rtsp://192.168.1.101/stream
requires: helmet, goggles, safety_vest
📷 Exit Zone
/dev/video0 (webcam)
requires: helmet
How it works:
One Process per camera — true parallel execution
Auto-restart crashed workers every 10 seconds
All cameras write to one SQLite DB (WAL mode)
SIGINT/SIGTERM graceful shutdown handler
Per-camera overrides for PPE rules and thresholds
🐳 Docker Deployment
# CPU — pipeline + dashboard docker compose up --build # NVIDIA GPU docker compose -f docker-compose.yml \
-f docker-compose.gpu.yml up
📦
CPU build —
python:3.11-slim base, runs on any machine
⚡
NVIDIA GPU —
pytorch/pytorch:2.3.0-cuda12.1 base, FP16 inference
🚀
~160 FPS —
FP16 on RTX A5000 — 11× faster than CPU baseline
🔄
ONNX/TensorRT —
Export for edge deployment, minimal latency

## Slide 10
WhatsApp Alert Integration — Meta Cloud API
10 / 12
📱 WhatsApp
🚨 PPE VIOLATION ALERT
📍 Gate-1 Camera
👤 Worker ID: W-03
🕐 14:32:11
❌ Missing PPE:
• Helmet
• Safety Vest
⚠️ Severity: CRITICAL
📸 Screenshot attached
─────────────────
🏭 Tata Steel — Zone A
🔗 Direct Meta Graph API
Calls Graph API v19.0 directly — no third-party SDK, no Twilio. Zero recurring cost beyond Meta's free tier.
📸 Screenshot attached
Every alert includes a JPEG of the violation frame, uploaded via the media API before sending the message.
🔕 Smart cooldown
Cooldown check runs BEFORE media upload — saves API quota. Same worker won't re-alert for 60 seconds.
🏷️ Camera label in every alert
Each camera has a configurable label in cameras.yaml. Security team sees exactly which zone triggered the alert.
👥 Multi-recipient + groups
Comma-separated E.164 phone numbers in .env. Supports group chat IDs for team notifications.

## Slide 11
Live Test Results & Demo
11 / 12
✅ Verified Results
🎯 Detection accuracy
Helmet, vest, goggles detected correctly on 366 test images at mAP 0.978
⚡ Alert latency
Alert fired within 8 frames of non-compliance (~0.27 s at 30 FPS)
📱 WhatsApp delivery
Message + screenshot delivered to phone in ~3 seconds
📊 Dashboard update
WebSocket pushed new alert to browser in < 0.5 seconds
📹 Video sources tested
Webcam (USB), MP4 file (IMG_9343.MOV), RTSP stream (simulated)
⚠️ Known Limitation
Clear / transparent safety goggles are not reliably detected.
The model was trained predominantly on tinted industrial goggles from Roboflow datasets. Clear goggles appear transparent against skin/clothing, lacking the contrast needed for detection.
Fix: Collect ~100 annotated images of clear goggles → fine-tune 20-30 epochs
🖥️ Test Environment
Hardware:
Apple MacBook Pro M1 Pro
OS:
macOS 14 (Sonoma)
Python:
3.12.2
PyTorch:
2.9.0 (CPU / MPS)
Inference:
336 ms/image on CPU (M1 Pro)

## Slide 12
Conclusion & Future Work
12 / 12
✅ Achievements
✓
Full 7-stage system built end-to-end and deployed
✓
mAP@0.5 = 0.978 on 366-image test set (Precision 0.980, Recall 0.970)
✓
Real-time violation alerts with < 1-second pipeline latency
✓
Multi-camera support via cameras.yaml — auto-restart on crash
✓
Docker CPU + NVIDIA GPU builds with FP16 / TensorRT export
✓
WhatsApp integration via Meta Cloud API — screenshot + message in 3s
✓
Live FastAPI dashboard with WebSocket, dark SPA — no build step
✓
Production-ready SQLite WAL logging with sessions + violations tables
🚀 Future Work
🎯
ByteTrack multi-object tracking for stable, persistent worker IDs across frames
📍
Zone-specific PPE rules — welding bay requires goggles, general floor requires helmet + vest
👓
Retrain with clear/transparent goggles — collect ~100 annotated images, fine-tune 20-30 epochs
🗄️
PostgreSQL for multi-site deployments — replace SQLite when scaling across factories
📱
Mobile app for security supervisors with push notifications and real-time camera switching
🌐 github.com/bytebender77/PPE-compliance-monitoring-system
Kunal Kumar Gupta · 23MC3035 · M.Tech CSE · RGIPT · 2026
Thank You